## Slide 1: Computer Networks
Network Layer

## Slide 2: Network Layer
Main function of Network Layer:
  Routing of packets form the source machine to the destination machine.

## Slide 3: Network Layer Design Issues
Store-and-forward packet switching
Services provided to transport layer
Implementation of connectionless service
Implementation of connection-oriented service
Comparison of virtual-circuit and datagram networks

## Slide 4: Store-and-Forward Packet Switching
The environment of the network layer protocols.
ISP’s equipment

## Slide 5: Services Provided to the Transport Layer
Services independent of router technology.
Transport layer shielded from number, type, topology of routers.
Network addresses available to transport layer use uniform numbering plan
  even across LANs and WANs

## Slide 6: Implementation of Connectionless Service
Routing within a datagram network
ISP’s equipment
A’s table (initially) A’s table (later) C’s Table E’s Table

## Slide 7: Implementation of Connection-Oriented Service
Routing within a virtual-circuit network
ISP’s equipment
A’s table C’s Table E’s Table

## Slide 8: Comparison of Virtual-Circuit and Datagram Networks
Comparison of datagram and virtual-circuit networks

## Slide 9: Routing Algorithms
Optimality principle
Shortest path algorithm
Flooding
Distance vector routing
Link state routing
Routing in ad-hoc networks

## Slide 10: Routing Algorithms
Broadcast routing
Multicast routing
Anycast routing
Routing for mobile hosts
Routing in ad hoc networks

## Slide 11: Routing Algorithms
Routing Algorithm:
  Network Layer Software responsible for deciding which output line an incoming packed should be transmitted on.
    Datagrams:
      require computation of decision making tables for each packed
    Virtual Circuit:
      routing decision are made only when a new virtual circuit is being set up.
    Session Routing:
      data packets follow the same routing for the entire session.

## Slide 12: Routing Algorithms
  Routing vs. Forwarding:
    Routing:
      Filling and Updating routing tables
    Forwarding:
      making the decision which routes to use based on routing tables.
  Adaptive vs. Non-Adaptive Algorithms.
    Non-Adaptive Algorithms:
      Routing decision is based on pre-computed measurements or estimates and do not update the table based on current traffic and topology
    Adaptive Algorithms:
      Change their routing decisions to reflect changes in the topology and traffic.

## Slide 13: Fairness vs. Efficiency
Network with a conflict between fairness and efficiency.

## Slide 14: Optimality Principle
If router J is on the optimal path from router I to router K, then the optimal path form J to K also falls along the same (optimal path) route.
  r1: I to J graph
  r2: The rest of the graph
  If a route better than r2 existed from J to K it could be concatenated with r1 to improve the route from J to K! Contradiction with the base assumption that r1r2 are optimal.

## Slide 15: The Optimality Principle
(a) A network. (b) A sink tree for router B.

## Slide 16: Shortest Path Routing
Optimization criterion:
  Distance,
  Bandwidth,
  Average Traffic
  Communication cost,
  Mean Queue Length,
  Measured Delay, …
Algorithms:
  Dijkstra
  Flooding
    Selective Flooding

## Slide 17: Shortest Path Algorithm
The first five steps used in computing the shortest path from A to D. The arrows indicate the working node

## Slide 18: Shortest Path Algorithm
Dijkstra’s algorithm to compute the shortest path through a graph.
. . .

## Slide 19: Shortest Path Algorithm (3)
Dijkstra’s algorithm to compute the shortest path through a graph.
. . .
. . .

## Slide 20: Shortest Path Algorithm
Dijkstra’s algorithm to compute the shortest path through a graph.
. . .

## Slide 21: Distance Vector Routing
Static Routing Algorithms
  Do not take into account actual network load.
Dynamic Routing Algorithms
  Taking into account actual network load
  Distance Vector Routing: Each router maintain a table with the best known distance to each destination and which line to use to get there. Tables updated by exchanging information with the neighbors.
  Link State Routing

## Slide 22: Distance Vector Routing
(a) A network. (b) Input from A, I, H, K, and the new routing table for J.

## Slide 23: Count–to-Infinity Problem
Slow Convergence to the correct answer.
“Good news” Propagate fast
“Bad news” Propagate slowly:
  The core of the problem is that when X tells Y that I has a path somewhere, Y has no way of knowing whether it itself is on the path.

## Slide 24: The Count-to-Infinity Problem
The count-to-infinity problem

## Slide 25: Link State Routing
Distance Vector Routing was used in the ARPANET until 1979 – when it was replaced by link state routing.
  Delay Metric was Queue Length thus did not take into account line bandwidth when choosing routes.
    Problem when line bandwidth changed for some bands from 56 kbps to 230 kbps or 1.544 Mbps.
    Algorithm took to long to converge (the count-to-infinity problem).
    Solution: Link State Routing

## Slide 26: Link State Routing (2)
Each router must do the following:
  Discover its neighbors and learn their network addresses.
  Measure the delay or cost to each of its neighbors.
  Construct a packet telling all it has just learned.
  Send this packet to all other routers.
  Compute the shortest path to every other router.
Complete topology and all delays are experimentally measured and distributed to every router. Dijkstra’s algorithm can be run to find the shortest path to every other router.

## Slide 27: (1) Learning About the Neighbors
“HELLO” packed send on each point-to-point line from a booted router.
Router on the other end must reply by sending its globally unique “name”.
Example of routers connected by a LAN.

## Slide 28: (1) Learning About the Neighbors
Nine routers and a LAN:
One way to model LAN is to consider it as node (Graph model).
B
A
D
C
G
F
E
F
Router
I
Routers connected to LAN
Graph Model
A
N
B
C
D
E
F
I
G
H

## Slide 29: (2) Measuring Line Cost
It is required by the Link State Routing algorithm that each router not have a reasonable estimate of the delay/cost to each of its neighbors.
  Send “ECHO” packet (ping) that the other side is required to send back immediately.
    Measure Round Trip time; Divide by 2 to get an estimate.
    More accurate estimate by repeating the process several times and by averaging estimates.
    Assumes symmetric delay.
Channel Load Issue when Measuring Delay
  To factor the load in: round trip timer must be started when the ECHO packed is queued.
  To ignore the load: round trip timer must be started when ECHO packed reaches front of the queue.

## Slide 30: (2) Measuring Line Cost (cont.)
Including Traffic-induced Delays:
  If a router has a choice from 2 lines with the same bandwidth, one of which is heavily loaded all the time and one of which is not, the router will regard the route over the unloaded line as shorter path. This choice in general will result in better performance
  Problem with Oscillations in the choice of best path.

## Slide 31: (2) Measuring Line Cost (cont.)
A
B
C
D
E
I
J
F
H
G
West
East

## Slide 32: (3) Building Link State Packets
Packet Format:
  Identity of Sender
  Sequence Number
  Age
  List of Neighbors
  Corresponding Delay
Packets easily built – problem with knowing when to built them.
A | 
Seq. | 
Age | 
B | 4
E | 5
E
A
B
C
D
F
4
2
3
4
6
8
1
5
B | 
Seq. | 
Age | 
A | 4
C | 2
F | 6
C | 
Seq. | 
Age | 
B | 2
D | 3
E | 1
E | 
Seq. | 
Age | 
A | 5
C | 1
F | 8
F | 
Seq. | 
Age | 
B | 6
D | 4
E | 8
D | 
Seq. | 
Age | 
C | 3
F | 4

## Slide 33: (4) Distributing the Link State Packets
Distributing Link State Packets Reliably is tricky:
  As the packets are distributed and installed, the routers getting the first ones will change their routes before other routers in the network update their routing tables.
  Different Routers may be using different versions of the topology (inconsistencies, loops, unreachable machines, etc.)
Basic Algorithm: Flooding
  Sequence Number (incremented for each new packet sent) is used to keep the flood in check.
  Routers keep track of all the source router packets they have been sent to.
  New link state packets is checked against the track list:
    If new/unseen (based on the sequence number) then it is broadcasted to all neighboring routers with exception of the sender.
    If duplicate, it is disregarded.
    If sequence number is lower than the highest one in the track list, it is rejected.

## Slide 34: (4) Distributing the Link State Packets (cont)
Problems with basic algorithm:
  Sequence Number wrap around.
    Make a long precision number (e.g., 32-bit)
  Crash of a router: losing track of sequence number.
  Corruption of sequence number.
Solution: Include Age of each packet.
  Decrement this value once per second.
  When zero, this state information is disregarded.
  Normally a new packed is send every 10 sec.
    Router information times out when:
      Router is down, or
      A Number of (e.g., 6) consecutive packets have been lost.

## Slide 35: (4) Distributing the Link State Packets (cont)
Refinements of Distribution Algorithm:
  Holding the packet:
  Example of packed buffer for router B of subnet in previous figure (Fig. 5-13 (a))
 |  |  | Sent Flags |  |  | Acknowledged Flags |  |  | 
Source | Seq. | Age | A | C | F | A | C | F | Data
A | 21 | 60 | 0 | 1 | 1 | 1 | 0 | 0 | 
F | 21 | 60 | 1 | 1 | 0 | 0 | 0 | 1 | 
E | 21 | 59 | 0 | 1 | 0 | 1 | 0 | 1 | 
C | 20 | 60 | 1 | 0 | 1 | 0 | 1 | 0 | 
D | 21 | 59 | 1 | 0 | 0 | 0 | 1 | 1 | 

## Slide 36: Hierarchical Routing
Large Networks:
  Proportionally large routing tables are required for each router
  More CPU time is needed to scan them
  More bandwidth is needed to send status reports.
  At certain point network may grow so large where it is no longer feasible for every router to have an entry for every other router.
  Solution: Routing has to be done hierarchically.

## Slide 37: Hierarchical Routing (cont.)
Routers divided in Regions (as in telephone network):
  Each router knows how to route packets to destinations within its own region.
  However, router does not have any information regarding the topology of the network of other regions.
When different networks are interconnected they are regarded as a separate region in order to free the routers in one network from having to know the topological structure of the other ones.
Huge networks will require more than two-level hierarchy.
How many hierarchical levels are optimal.
  Kamoun and Kleinrock (1979): optimal number for an N router subnet is ln(N), requiring total of e*ln(N) entries per router.

## Slide 38: Hierarchical Routing (cont.)
Example: Berkley, California Router to Malindi, Kenya.
  Berkley to Los Angeles router (in-state traffic)
  Los Angeles to New York router (out-of-state traffic)
  New York to Nairobi (international traffic) …

## Slide 39: Two Level Hierarchical Routing Example
Region 1
Full table for 1A |  | 
Dest. | Line | Hops
1A | - | -
1B | 1B | 1
1C | 1C | 1
2A | 1B | 2
2B | 1B | 3
2C | 1B | 3
2D | 1B | 4
3A | 1C | 3
3B | 1C | 2
4A | 1C | 3
4B | 1C | 4
4C | 1C | 4
5A | 1C | 4
5B | 1C | 5
5C | 1B | 5
5D | 1C | 6
5E | 1C | 5
1A
1B
1C
2A
2B
2C
2D
4B
4A
4C
5B
5C
5E
5D
5A
3A
3B
Region 2
Region 3
Region 4
Region 5
Hierarchical table for 1A |  | 
Dest. | Line | Hops
1A | - | -
1B | 1B | 1
1C | 1C | 1
2 | 1B | 2
3 | 1C | 2
4 | 1C | 3
5 | 1C | 4

## Slide 40: Broadcast Routing
Sending a packed to all destinations simultaneously is called Broadcasting.
  Direct Method: Source sends a distinct packet to each destination routers in the subnet:
    Wasteful of the bandwidth.
    It requires source to have a list of all destinations.
    In practice this may be the only feasible solution.
  Flooding:
    Ordinarily ill suited for point-to-point communication:
      Generates to many packets, and
      Consumes to much bandwidth.

## Slide 41: Broadcast Routing (cont.)
  Multi-destination Routing
    Each packets contains:
      A list of designations, or
      A bit map indicating the desired destinations.
    When packet arrives at a router:
      The router checks all the destinations to determine the set of output lines that will be needed.
      Generates a new copy of the packed for each output line to be used and includes in each packet only those destinations that are to use the line.
      After a sufficient number of hops, each packed will carry only one destination and can be treated as normal packet.
    Multi-destination routing is like separately addressed packets, except that when several packets must follow the same rout, one of them pays full fare and the rest ride free.

## Slide 42: Broadcast Routing (cont.)
Spanning Tree:
  It is a subset of the subnet that includes all routers but contains no loops.
  Each router knows which of its lines belong to the spanning tree, it can copy an incoming broadcast packet onto all the spanning tree lines except the one it arrived on.
    Makes excellent use of bandwidth (generates absolute minimum number of packets necessary to do the job)
    Must have knowledge of some spanning tree for the method to be applicable.
      Information available in some instances (e.g., link state routing)
      Information not available (e.g., distance vector routing)

## Slide 43: Broadcast Routing (cont.)
Reverse Path Forwarding:
  Router checks if the broadcast packet arrived on the line that is normally used for sending packets to the source of the broadcast.
  If so, there is excellent chance that the broadcast packet itself followed the best route from the router and is therefore the first copy to arrive at the router. The router forwards copies of it onto all lines except the one it arrived on.
  If the broadcast packet arrived on a line other than the preferred one for reaching the source, the packet is discarded as a likely duplicate.

## Slide 44: Broadcast Routing (cont.)
Example of Reverse path Forwarding
A
B
C
D
G
J
O
M
N
L
K
H
E
I
F
A
B
C
D
G
J
O
M
N
L
K
H
E
I
F
A subnet
A sink tree for router I

## Slide 45: Broadcast Routing (cont.)
The tree build by reverse path forwarding. After 5 hops and 24 packets the broadcasting terminates compared to 14 packets had the sink tree been followed exactly
I
F
H
J
N
A
D
E
C
B
G
O
M
K
L
L
H
G
E
K
D
N
H
O
B

## Slide 46: Broadcast Routing (cont.)
Reverse Path Forwarding in spite of not being optimal procedure:
  Efficient and easy to implement Algorithm
  It does not require routers to know about spanning trees.
  Does not have the overhead of destination list or bit map in each broadcast packet (as multi-destination addressing).
  It does not require any special mechanism to stop the process as flooding does (hop counter in each packed and a priori knowledge of the subnet diameter, or a list of packets already seen per source)

## Slide 47: Multicast Routing
Application that require separate processes (i.e., each from separate location) access and ability to work on the same data.
  Small group can use point-to-point messaging to accomplish this task.
  Broadcasting can be used but communicating with 1000 “interested” machines out of million-node network is inefficient.
Need a mechanism that would send messages to well-defined groups that are numerically large in size but small compared to the network as a whole.
  Sending a message to a such a group is called multicasting.
  Corresponding routing algorithm is called multicast routing.

## Slide 48: Multicast Routing (cont)
Requirements:
  Create and Destroy Groups
  Nodes should be able to Join and Leave Groups, etc.
    Group Management.
  When a process joins a group it informs its host.
  Routers must know which of their hosts belong to which group.
    Host must inform their routers about changes in group membership, or
    Routers must query their hosts periodically.
  Information shared with Neighboring Routers (propagation of information through the subnet).

## Slide 49: Multicast Routing (cont)
Each Router Computes Spanning Tree Covering all other routers.
Example of a network with nodes belonging to two groups (1 & 2).
1,2
1,2
1
1
1
2
2
2
Network
2
1
1
1
1
1
A Multicast Tree for group 1
1,2
1,2
1
1
1
2
2
Spanning Tree for the leftmost Router
2
2
2
2
2
A Multicast Tree for group 2
2

## Slide 50: Multicast Routing Tree Pruning
Link State Routing – each router is aware of the complete topology, including which hosts belong to which groups.
  Pruning starting from leaf-node up toward root node.
Distance Vector Routing – Basic pruning algorithm is based on reverse path forwarding.
  Router with no hosts interested in a particular group and no connections to other routers responds with PRUNE message to a multicast message.
  Also when a router with no group members among its hosts receives a multicast message it too will respond with a PRUNE message effectively recursively pruning the subnet.
  Potential Problem:
    Scales poorly to large networks.
      Network with n groups,
      Each Group on average has m members.
      For each Group m – spanning trees must be stored; total of m*n trees.
      Significant storage requirements for large number of groups.

## Slide 51: Multicast Routing Tree Pruning
Core-Based Trees – an alternative algorithm:
  Uses one spanning tree per group,
  Root (core) node near the middle of the group.
  Host sends multicast message to core node; which in turn sends the message along the spanning tree.
    Tree will not be optimal for every source,
    Reduction is storage from m trees to one tree per group.

## Slide 52: Multicast Routing Tree Pruning
Core-based tree for group 1.
Sending to group 1.

## Slide 53: ANyCast Routing
Delivery models in which a source sends to a single destination (called unicast) to all destination (called broadcast) have been discussed so far.
Another method that is useful is called anycast in which a packed is delivered to the nearest member of a group.
Why one would want anycasting?
  Sometimes nodes provide a service, such as time of day or content distribution for which it is getting the right information all what is required (not the node that is connected too).

## Slide 54: Anycast Routing
Anycast routes to group 1.
Topology seen by the routing protocol.

## Slide 55: Routing for Mobile Hosts
Increasing number of users of Portable Computers and Personal Computer Devices. They require access to:
  E-mail
  File System, etc.
In order to route a packet to a mobile host, the network first has to find it.
World Model of communication network:
  WAN consisting of routers and hosts,
  LAN’s connected to WAN, and
  MAN’s connected to WAN.

## Slide 56: Routing for Mobile Hosts (cont)
A WAN to which LAN’s, MAN’s and wireless cells are attached:
Wireless cell
Foreign LAN
Foreign Agent
Mobile Host
MAN
Home LAN
Home Agent
WAN

## Slide 57: Routing for Mobile Hosts (cont)
Stationary Hosts:
  Hosts that never move.
Migratory Hosts:
  Stationary hosts who move from one fixed site to another from time to time but use the network only when they are physically connected to it.
Roaming Hosts:
  Need to maintain their connections as they move around.
Mobile Hosts:
  Migratory and Roaming Hosts – that is all host that are away from home and still want to be connected.

## Slide 58: Routing for Mobile Hosts (cont)
All hosts are assumed to have:
  A permanent home location, and
  A permanent home address:
    Used to determine their home location (analogous to telephone number; e.g., 1-212-555-1212).
Routing goal in systems with mobile hosts:
  To make possible to send packets to mobile hosts using their home address, and
  Have the packets efficiently reach them wherever they may be.
Trick is off course to find them first.

## Slide 59: Routing for Mobile Hosts (cont)
According to the sketch in previous slide world is divided up (geographically) into small units – areas.
  Areas are typically LANs or wireless cells.
  Each area has one or more
    Foreign agents:
      Processes that keep track of all mobile hosts visiting the area.
    Home agent:
      Keeps track of hosts whose home is in the area, but who are currently visiting another area.
REGISTRATION with Foreign Agent: When a new host enters an area, either by connecting to it (e.g., plugging into LAN), or wandering into the cell it must register itself with the foreign agent of that area.

## Slide 60: Registration Procedure of Mobile Hosts
Each foreign agent broadcasts periodically a packet announcing its existence and address.
  Newly-arrived mobile host may:
    Wait for one of these message, or if none arrives quickly enough
    Can broadcast a packet “saying”: Are there any foreign agents around?
The mobile host registers with the foreign agent:
  Gives its home address,
  Current data link layer address, and
  Some security information.

## Slide 61: Registration Procedure of Mobile Hosts
The foreign agent contact the mobile host’s home agent and informs it about a mobile host in his area. This message contains:
  The foreign agent’s network address,
  Security information (“to convince the home agent that the mobile host is really there”).
The home agent authenticates security information containing:
  Timestamp (to prove that it was generated within the past few seconds), etc.
  Acknowledges foreign agent by indicating to proceed if everything checks out.
Foreign agent registers and informs the mobile host.

## Slide 62: Registration Procedure of Mobile Hosts
Checking out when done (typically mobile hosts just turn-off their computers).

## Slide 63: Packet Routing for Mobile Hosts Example of sending a packed to a mobile host that has been registered.
1. Packet is sent to the mobile host’s home address
2. Packet is tunneled to the foreigh agent
3. Sender is given foreign agent’s address
4. Subsequent packets are tunneled to the foreign agent

## Slide 64: Packet Routing for Mobile Hosts
Example: Sender wants to send a packet to a host in New York.
  Packets sent to the mobile host on its home LAN in NEW York are intercepted by the home agent (step 1).
  Home agent looks up mobile host’s new (temporary) location and finds the address of the foreign agent handling the mobile host (i.e., Los Angeles).
  Home agent does:
    It encapsulates the packet in the payload field of an outer packet and sends the latter to the foreign agent (step 2). This mechanism is called tunneling. After getting the encapsulated packet, the foreign agent removes the original packet from the payload field and sends it to the mobile host as a data link frame.
    The home agent tells the sender to henceforth send packet to the mobile host by encapsulating them in the payload of packets explicitly addressed to the foreign agent instead of just sending them to the mobile host's home address (step 3.) Subsequent packets can now be routed directly to the host via foreign agent (step 4.), bypassing the home agent entirely.

## Slide 65: Routing in Ad Hoc Networks
Ad Hoc networks refers to the extreme case of mobility where not only the hosts are mobile but routers as well. Examples:
  Military vehicles on a battlefield with no existing infrastructure.
  A fleet of ships at sea.
  Emergency workers at en earthquake that destroyed the infrastructure.
  A gathering of people with notebook computers in an area lacking 802.11 (IEEE Wireless LAN protocol).

## Slide 66: Routing of Ad Hoc Networks (cont)
Each node consists of a router and a host – usually on the same computer.
Networks of neighboring nodes are called ad hoc networks or MANETs (Mobile Ad-hoc NETworks).
Features of such networks:
  Routers come and go or appear in new places all the time.
  Consequently, Network Topology may be changing all the time.
  Validity of paths can thus change spontaneously.

## Slide 67: Ad hoc On-demand Distance Vector routing (AODV) Algorithm
AODV takes into account limited bandwidth and low battery life of devices.
It is a on-demand algorithm; that is it determines a route to some destination only when there is a demand to send a packed to a destination.

## Slide 68: Ad hoc On-demand Distance Vector routing (cont)
Route Discovery
  Ad-hoc network can be described by a graph of the nodes (routers + hosts).
  Two nodes are connected (depicted via an connecting arc in the graph) if they can communicate directly using their radios.
  For simplicity connection is assumed symmetric (e.g., case where node A has a more powerful transmitter then node B thus node A can communicate to B but not vice versa is not considered).

## Slide 69: Ad hoc On-demand Distance Vector routing Example
A
B
C
D
G
E
F
H
I
Range of A’s Broadcast
Range of A’s Broadcast
A
B
C
D
G
E
F
H
I
After B and D have received of A’s Broadcast
A
B
C
D
G
E
F
H
I
After C,F and G have received of A’s Broadcast
A
B
C
D
G
E
F
H
I
After E,H and I have received of A’s Broadcast

## Slide 70: AODV Algorithm
Scenario: A wants to send a packet to node I.
AODV algorithm maintains a table at each node keyed by destination giving information about that destination including which neighboring node to send packets to in order to reach the destination.
Suppose node A can not find the information about destination node I. Thus it needs to discover a route to node I.
Algorithm Details.

## Slide 71: AODV Algorithm (cont)
To locate an unknown node (I), source node A constructs a special ROUTE REQUEST packet and broadcasts it.
The packed reaches A’s neighboring nodes B and D. B and D at this time are directly communicating with A (as opposed to F for example).
Format of ROUTE REQUEST PACKET:
  Source and Destinations Address (typically IP address).
  Request ID – local counter maintained separately by each node and incremented each time a ROUTE REQUEST is broadcast.
  Source Address and Request ID uniquely identify the ROUTE REQUEST packet. This allow nodes to discard any duplicate packets they may receive.
  Sequence Counters – Each node also maintains a second sequence counter incremented whenever a ROUTE REQUEST is sent (or a reply to someone's else’s ROUTE REQUEST) . It is used to tell new routes form old routes.
  Hop Count – keeps track of how many hops the packet has made.
Source Address
Request ID
Destination Address
Source Sequence #
Destination Sequence #
Hop Count

## Slide 72: AODV Processing on a node (cont)
When ROUTE REQUEST packet arrives at a node (B & D in this case), it is processed in the following steps:
  The Source Address, Request ID pair is looked up in local history table to see if this request has already been seen and processed.
    If duplicate – it is disregarded
    If not duplicate – pair is entered in history table.
  The receiver node looks up the destination in its route table. If a fresh route to the destination is know, a ROUTE REPLY packet is sent back to the source informing it how to get to the destination. Fresh means that the Destination sequence number stored in the routing table is greater than or equal to the Destination sequence number in the ROUTE REQUEST packet. If it is less, the stored route is older than the previous route the source had for the destination thus next step 3 is executed.
A
B
C
D
G
E
F
H
I
After B and D have received of A’s Broadcast

## Slide 73
  Since the receiver node does not know a fresh route to the destination, it:
    Increments the Hop count field,
    Rebroadcast the ROUTE REQUEST packet to its neighboring nodes with exception to node from which it has received it.
    Extracts the data from the packed and stores it as a new entry in its reverse route table. This information will be used to construct the reverse route so that the reply can get back to source later as specified with reverse arrows.
    A timer is started for the newly-made reverse route entry. If it expires the entry is deleted.
A
B
C
D
G
E
F
H
I
After C,F and G have received of A’s Broadcast

## Slide 74: AODV Algorithm (cont)
Since neither B nor D knows where I is, each creates reverse route entry pointing back to A, and broadcasts the packet with Hop count set to 1.
Broadcast from B reaches C and D.
  C makes an entry for it in its reverse route table and rebroadcasts it.
  D in contrast rejects it as a duplicate.
Broadcast from D’s
  is rejected by B as a duplicate, however,
  it is accepted by F and G.
A
B
C
D
G
E
F
H
I
After C,F and G have received of A’s Broadcast

## Slide 75: AODV Algorithm (cont)
After E, H, and I receive the broadcast, the ROUTE REQUEST finally reaches a destination that knows where I is, namely I itself.
Note: Broadcast from each node are not coordinated in any way.
A
B
C
D
G
E
F
H
I
After E,H and I have received of A’s Broadcast

## Slide 76: Reply Packet in AODV
In response to the incoming request, I builds a ROUTE REPLY packet and:
  The Source address, Destination address, Hop Counter are copied from the incoming request.
  Destination sequence number is taken from its counter.
  The Hop count field is set to 0.
  The Lifetime field controls how long the route is valid.
This packed is cast back to the node that ROUTE REQUERST packed came form, in this case node G.
From G it follows the reverse path to D and finally to A. At each node Hop count is incremented so the node can see how far from the destination (I) is.
Source Address
Destination Address
Life-time
Destination Sequence #
Hop Count

## Slide 77: Reply Packet in Intermediate nodes
At each intermediate node the packed is inspected and entered into local routing table as a route to I if one or more of the following three conditions are met:
  No route to I is known.
  The sequence number for I in the ROUTE REPLY packed is greater than the value in the routing table.
  The sequence numbers are equal but the new route I s shorter.
This ensures that all nodes on the reverse route learn the route to I for free as a byproduct of A’s route discovery.
Nodes that got the original REQUEST ROUTE packed but were not on the reverse path (B, C, E, F, and H in this example) discard the reverse route table entry when the associated timer expires.

## Slide 78: Route Maintenance
In Ad-hoc networks the nodes can move or can be switched off.
  For example if G is switched off, A will need to deal with it because the route that it was using (ADGI) is no longer valid.
  Idea: each node broadcasts a Hello message periodically. Each neighbor is expected to respond to it. For the cases that there is no response the information is purged for the routes that use corresponding node.
  List of Active Neighbors for a destination: For each possible destination, each node, N, keeps track of its neighbors that have fed it a packed for that destination during the last ∆T seconds.
    A node N does this by having a routing table keyed by destination containing:
      Outgoing node to use to reach that destination,
      Hop count to the destination
      Most recent destination sequence number, and
      The list of active neighbors for that destination.

## Slide 79: Example of a Routing Table
Dest. | Next hop | Distance | Active Neighbors | Other fields
A | A | 1 | F,G | 
B | B | 1 | F,G | 
C | B | 2 | G | 
E | G | 2 |  | 
F | F | 1 | A,B | 
G | G | 1 | A,B | 
H | F | 2 | A,B | 
I | G | 2 | A,B | 
D’s routing table before G goes down
Graph after G has gone down
A
B
C
D
G
E
F
H
I

## Slide 80: Route Maintenance (cont)
When any of N’s neighbors becomes unreachable, it checks its routing table to see which destinations have routes using this node. For each of these routes, the active neighbors are informed that their route via N is now invalid and must be purged from their routing tables.
The active neighbors nodes propagate this information to their active neighbors, and so on recursively, until all routes depending on the unavailable node are purged from all routing tables.

## Slide 81: Congestion Control Algorithms
The situation when to many packets are present in subnet it is called congestion.

## Slide 82: Approaches to Congestion Control
Timescales of approaches to congestion control

## Slide 83: Traffic-Aware Routing
A network in which the East and West parts are connected by two links.

## Slide 84: Congestion Factors
Streams of inputs packets arriving from multiple lines (3-4 or more) needing the same output line => queue buildup.
  Adding more memory may help to a point but – a study by Nagle suggest that increasing memory to ∞ to accommodate larger queues congestions gets worse not better due to time required to get to the front of the queue (timed out).
Slow Processors:
  Queue build up due to routers slow CPU’s at performing bookkeeping task:
    Queueing buffers,
    Updating tables, etc.
Low bandwidth lines.
Typically the problem is that upgrading one part of the system shifts the bottleneck to the other someplace else. The real problem frequently is a mismatch parts of the system. The problem will persist until all components of the system are in balance.

## Slide 85: Congestion Control vs. Flow Control
Congestion Control has to due with making sure the subnets are able to carry the offered traffic. Thus it is a global issue involving the behavior of
  all the hosts,
  all the routers,
  the store-and forwarding processing within the routers, and
  all the other factors that tend to diminish the carrying capacity of the subnet.
Flow Control relates to point-to-point traffic between a given sender a given receiver. Its job is to make sure that a fast sender cannot continually transmit data faster than the receiver is able to absorb it.
  It frequently involves some direct feedback from the receiver to the sender to tell the sender how things are doing at the other end.

## Slide 86: Congestion Control vs. Flow Control Example
Flow Control Problem: Consider a fiber optic network with a capacity of 1000 Gbps on which a supercomputer is trying to transfer a file to a personal computer at 1 Gbps. Although there is not congestion the supercomputer has to frequently stop in order to allow PC to catch up.
Congestion Control Problem: Consider a store-and-forward network with 1 Mbps lines and 1000 large computers, half of which are trying to transfer files at 100 kbps to the other half creating a traffic of 500x100 kbps = 50000 kbps = 50 Mbps. The problem here is that this traffic exceeds the capacity of what the network can handle.

## Slide 87: General Principles of Congestion Control
Analogy with Control Theory:
  Open-loop, and
  Closed-loop approach.
Open-loop approach
  Problem is solved at the design cycle
  Once the system is running midcourse correction are NOT made.
  Tools for doing open-loop control:
    Deciding when to accept new traffic,
    Deciding when to disregard packets and which ones.
    Making scheduling decision at various points in the network.
    Note that all those decisions are made without regard to the current state of the network.

## Slide 88: General Principles of Congestion Control
Closed-loop approach
  It is based on the principle of feedback-loop. The approach has three parts when applied to congestion control:
    Monitor the system to detect when and where congestion occurs,
    Pass this information tot places where action can be taken
    Adjust system operation to correct the problem.

## Slide 89: General Principles of Congestion Control
Monitoring - Metrics to be used to monitor subnet congestion:
  Percentage of all packets disregarded for lack of buffer space.
  Average queue length
  Number of packets that time out and are retransmitted,
  Average packet delay
  Standard deviation of packed delay.
Transferring congestion information
  Information send to the source(s) of the traffic. Undesirable because extra traffic is initiated when opposite is needed.
  Another approach is to reserve a bit field that can be set when congestion gets above some level of threshold.
  Routers/Hosts send periodically probe packets out to explicitly ask about congestion. This information can then be used to route traffic around problem areas.
  In general in all feedback schemes, the hope is that knowledge of congestion will cause the hosts to take appropriate action to reduce the congestion. Time constant in any adjustment scheme is critical and non-trivial problem:
    To fast adjustment is responsive but can lead to oscillations.
    To slow adjustment is response time is sluggish and of no real value.

## Slide 90: General Principles of Congestion Control
The presence of a congestion means that the load is (temporarily) greater than the resources (in part of the system) can handle.
  Increase Resources, and/or
  Decrease the Load.

## Slide 91: General Principles of Congestion Control
Increase of Resources:
  Use dial-up telephone lines to temporarily increase the bandwidth between certain points.
  On satellite systems increasing transmission power often gives higher bandwidth.
  Splitting traffic over multiple routes (instead of using the best one) may effectively the bandwidth.
  Use of spare routers that are normally used as backups to give more capacity.

## Slide 92: General Principles of Congestion Control
Decrease the Load
  It is not always possible to increase capacity of the subsystem. Thus the only other way to reduce congestion is to decrease the load.
    Denying service to some users (AOL in early days),
    Degrading service to some or all users,
    Having users schedule their demands in more predictable way.

## Slide 93: Congestion Prevention Policies Open-loop Approach
Open-loop system designed to minimize congestion in the first place rather then reacting after it happened.
Try to achieve this goal at various levels/layers:
Data Link Layer:
  Retransmission Policy:
    Sender with quick time out and go-back-n retransmitting packets vs.
    Selective repeat with slower time out.
  Out-of-order catching policy
  Acknowledgment policy
  Flow control policy

## Slide 94: Congestion Prevention Policies Open-loop Approach
Network Layer:
  Virtual circuit versus datagram inside the subnet:
    Many congestion control algorithms work only with virtual circuit subnets.
  Packet queueing and service policy:
    One queue per input line or output line or both.
    Processing the queue:
      Round-robin
      Priority based queue processing.
  Packet discard policy
    Bad policy can make the problem worse.
  Routing algorithm
    Spreading the traffic over all the lines can help, vs.
    Directing the traffic on the already congested line.
  Packet lifetime management – Deals with issue that determines how long a packet may live before it is disregarded.
    To long a life time lost packets may clog up the works for a long time.
    To short on the other hand packets may time out before even given a chance to reach the destination, thus inducing retransmission.

## Slide 95: Congestion Prevention Policies Open-loop Approach
Transmission Layer – same issues like in Data Link Layer with one addition determining the time out is harder because the transit time across the network is less predictable than the transit time over a wire between two routers.
  Retransmission Policy:
  Out-of-order catching policy
  Acknowledgment policy
  Flow control policy
  Time out determination

## Slide 96: Congestion Prevention Policies in Virtual-Circuit Subnets
Admission Control:
  Simple algorithm – once congestion has been signaled, no more virtual circuits are set up until the problem had gone away.
    Attempts to setup new transport layer connections will fail.
Alternate Approach to Admission Control:
  Allow new virtual-circuits but carefully route all new ones around the problem area,

## Slide 97: Alternate Approach to Admission Control Example
A
B
a)
A
B
b)
New Virtual-Circuit
(a) A congested network. (b) The portion of the network that is not congested. A virtual circuit from A to B is also shown.

## Slide 98: Traffic Throttling (2)
Explicit congestion notification

## Slide 99: Load Shedding (1)
A choke packet that affects only the source..

## Slide 100: Load Shedding (2)
A choke packet that affects each hop it passes through.

## Slide 101: Negotiated Approach to Congestion Control
Agreement is negotiated between the host and subnet when a virtual circuit is set-up.
  Agreement specifies:
    Volume and shape of the traffic,
    Quality of service requires, etc.
  Subnet guarantees the connection since it will make all necessary resource available during the set. Resource typically include:
    Table and buffer space in the routers, and
    bandwidth on the lines.
  Agreement can be done
    All the time as part of standard operating procedure (wastes resources), or
    Only when the subnet is congested.

## Slide 102
End